## Slide 1
Acoustic Source Localization
on a Wireless Sensor Node
Leke, undergraduate EE, University of Virginia
Supervisor: Ben
Summer 2026 | work in progress
Notes: Set expectations in one sentence: this is a progress report on a project that works end to end but is not finished, and you will be clear about which parts are proven and which are not.
If you have the array with you, hold it up here. It is small, and people are surprised by that.

## Slide 2
The goal
• A small node that hears a sound and reports the direction it came from
• Several nodes cross their bearings to locate a source
• This summer: ONE node, microphone to bearing in degrees
• The network part is not started. That is honest, not a spoiler
Notes: Explain the eventual system briefly so the audience knows where this is heading, then narrow immediately to what was actually built. Say the network part is not started now, so it is not a surprise later.
Reference design is SpeechCompass (CHI 2025), same microcontroller family and the same microphones.

## Slide 3
How direction comes out of timing
• Sound reaches the four mics at slightly different times
• Those differences depend on direction
• At 16 kHz one sample is 2.1 cm of travel
• So delays need sub-sample accuracy
• GCC-PHAT plus peak interpolation gets it
Notes: This is the physical core of the talk and worth spending time on. The punchline is sub-sample accuracy: whole-sample resolution is not enough, which is why the method is GCC-PHAT with an interpolated peak rather than simple peak finding.
PHAT means the correlation is weighted by phase, which makes it robust to the very uneven frequency content of a clap. If someone asks why not plain cross correlation, that is the answer, and there is a backup slide.

## Slide 4
System overview
• Four PDM MEMS mics, 16 kHz per channel
• STM32L552 at 96 MHz: DFSDM decimation, DMA into RAM
• Clap trigger, one second stored
• Bearing computed ON the board with CMSIS-DSP
• Raw audio also dumped over serial, on purpose
Two outputs from one capture is what makes validation possible: the board's answer and the samples that produced it
Notes: Walk the chain left to right once: mics, DFSDM, DMA, RAM, clap trigger, then it splits into the on-board localizer and the raw dump to a PC.
Emphasise that both paths exist deliberately. The board computes its own answer AND the raw audio comes out, so the same samples can be re-run against the reference implementation on a PC. Without that there would be no way to tell a firmware bug from a room problem.
Consider drawing the block diagram on the whiteboard as you say it.

## Slide 5
Four microphones on two data pins
• The chip has four DFSDM channels, not eight
• Each mic's SEL pin picks the rising or the falling clock edge
• Two mics with opposite SEL share one wire without colliding
• Mics 0 and 1 on PE7, mics 2 and 3 on PB1, one clock net to all four
This is the manufacturer's intended use of SEL, not a hack
Notes: A good 'clever bit' slide. The original plan assumed eight DFSDM channels; this part has four. Rather than change parts, the SEL pin fits four microphones into the pins available.
Mic drives the line while the clock is high if SEL is grounded, and while it is low if SEL is at 3V3, so the two never collide. Channel pin redirection inside DFSDM is what lets both halves of each pair be reached.
Finding the four-channel limit early rather than late is the reason the design fits at all.

## Slide 6
The problem that had to be solved first
• The four digital filters must start on the same clock edge
• If they do not, every channel carries an unknown offset
• An unknown offset is indistinguishable from real acoustic delay
• Fix: synchronized start, followers armed first, trigger filter last
The data cannot reveal this on its own, so it was tested directly
Notes: This is the single point of failure of the whole approach. Everything downstream measures time differences, so a constant per-channel offset poisons every result and still looks perfectly plausible.
Make the point that the system cannot detect this from a normal recording. That is exactly why the next slide exists: a test designed so that only a sync fault could produce a certain result.

## Slide 7
Proving synchronization before trusting anything
• Mics packed in a tight line, about 2 cm apart
• True delay across the whole array is then under 3 samples
• So a large offset could ONLY be a sync fault
• Measured: linear in mic position to 0.131 samples
• Fixture retired the day it passed
Notes: The design of the test is the point worth making, more than the numbers. A spread out array would have confounded a sync fault with real geometry. Packing the mics tight made the two separable, because at 2 cm spacing physics cannot produce a large delay.
The four measured delays were 0.000, -0.481, -1.354 and -1.801 samples, monotonic across the line and straight to within 0.131 samples.
That fixture could never localize anything, its aperture is under 3 samples, so it was retired immediately after it did its one job.

## Slide 8
Array geometry, and why it is not hardcoded
• Built array 9.25 x 9.9 cm, calipered port to port
• Layout changed twice mid-build, for physical reasons only
• So geometry lives in ONE registry file
• Condition number 1.07, so no blind directions
• Trying another layout is a one line change
Notes: The layout changed twice in a day: first only one breadboard was available, which forced a thin rectangle, then two were glued together and a near-square fit again. Nothing about the mathematics changed. That is why geometry was moved out of the analysis scripts into a registry with one active layout.
Measure port to port, not pin to pin: on a breakout board the mic port is offset from the header pins, and 1 mm is about 0.047 samples.

## Slide 9
Mean error alone is misleading
Layout | Aperture | Condition number | Mean | p90 | Worst
9.25 x 9.9 cm (BUILT) | 13.5 cm | 1.07 | 1.03 deg | 2.09 deg | 2.39 deg
9.25 x 12 cm | 15.2 cm | 1.30 | 0.70 deg | 2.01 deg | 2.16 deg
9.25 x 16 cm | 18.5 cm | 1.73 | 0.51 deg | 1.10 deg | 1.42 deg
10 cm square (sim reference) | 14.1 cm | 1.00 | 1.12 deg | 2.32 deg | 2.43 deg
2.8 x 10 cm (one breadboard) | 10.4 cm | 3.57 | 1.87 deg | 7.87 deg | 8.43 deg
2.5 cm square | 3.5 cm | 1.00 | 6.33 deg | 8.60 deg | 9.20 deg
Simulation only: 36 angles x 3 trials, 2 m source, 20 dB SNR. No reverberation, and the estimator is handed the exact geometry, so this RANKS layouts rather than predicts real accuracy.
Notes: The row to point at is the 2.8 x 10 cm single-board rectangle. Its MEAN is a respectable 1.87 degrees, but its p90 is 7.87 degrees, because the error is not spread evenly: it piles up in four narrow cones about 30 degrees off the long axis. Averaged over all directions that looks fine. If your source sits in one of those cones it is not fine.
Condition number predicts that directly, which is why the code warns based on it rather than on a hardcoded list of bad angles. Near 1 means uniform accuracy; above about 2 means blind directions exist.
The extreme case: a straight line of mics is rank 1, the across-axis component is unconstrained, and the estimator returns 0 or 180 degrees regardless of truth. The script hard-fails rather than print a plausible number.

## Slide 10
How correctness was established
• Build ONE trusted reference, check everything against it
• 1. Verify in simulation, where truth is known
• 2. Prove channel sync separately from geometry
• 3. Share code between the test and the reference so they cannot drift
• 4. Compare the embedded port to the reference on identical samples
Simulation: delay bias under 0.001 samples, angle error under 0.1 deg, about 0.4 deg at 0 dB SNR
Notes: This is the methodology slide and probably the most important one for a research audience.
The temptation in a localization project is to judge a result by whether the angle looks about right. That does not work, because plenty of bugs produce plausible angles. A wrong channel map, a sign error, a filter offset: all of them give you a number in degrees that could be true.
Point 3 is a small thing with a big payoff: the bring-up script imports GCC-PHAT from the reference rather than reimplementing it, so the test and the thing being tested cannot quietly drift apart.

## Slide 11
Result, and what dominated the error
At 65 cm the wall reflection arrived inside the analysis window and corrupted one specific mic pair. Moving to 2.1 m fixed it with no code change at all.
Notes: The best story in the project, so tell it as a story.
The first ground-truthed capture was 3.4 degrees off and one mic pair was inconsistent with the other five. The array was 65 cm from a wall. The reflection was arriving soon enough to land inside the 2048 sample analysis window, so the estimator was fitting a mixture of the direct sound and its echo.
Moving the array to 2.1 m of clearance took the error to +0.58 degrees, which is at the simulation's own accuracy floor. Nothing in the code changed.
This is why the capture folders record the room setup alongside the data: distance to the nearest wall is a property of the measurement, not of the run.

## Slide 12
A self-check that needs no ground truth
• Delay is antisymmetric: A to B, plus B to C, must equal A to C
• It does not, when a reflection has corrupted a pair
• Worst violation across all four triangles flags a bad capture
• Residual tracked the error: 0.119, 0.347, 0.499 samples
against errors of 0.6, 2.1 and 6.4 degrees
• The firmware flagged both bad captures on its own
Notes: The key property is that this needs no knowledge of the true angle, which makes it usable in the field and not only in a validation run. In a deployed node there is no protractor.
The firmware prints 'inconsistent: suspect a reflection' when the residual passes 0.3 samples, and it did so unprompted on both of the 315 degree trials before anyone had worked out why they were worse.
It is a consistency check, not a correctness check: a capture can be self-consistent and still wrong. But an inconsistent one is definitely suspect.

## Slide 13
Putting it on the microcontroller
Selective table mode names only the three tables a 4096 point real FFT needs. Final image 55.7 KB, with 48 KB of FFT buffers in a separate RAM section that costs no flash.
Notes: Good slide for showing that embedded work is largely about budgets.
CMSIS-DSP was vendored in by hand rather than added through the config tool, because the only available pack carrying it also switches on a USB device stack, a USB core and an AI application, all competing for the RAM the capture buffers need.
Then the size problem: compiled whole, the tables file is 707 KB, larger than the entire 512 KB flash. It holds twiddle and bit-reversal tables for every FFT length and data type, and the generic initializer references all of them, so the linker cannot drop any. Naming only the three tables actually needed took it to 40 KB.
Timing estimate is about 10 ms of FFT work per 32 ms frame at 96 MHz, so roughly 3x headroom.

## Slide 14
Every failure this summer was silent
What broke | What you saw | Actual cause
Config tool regeneration | Capture quietly wrong, twice | DMA reverted to Normal mode, later to Byte width
Serial dump | Only part of the recording arrived | Size argument is 16-bit: 128000 truncated to 62464
Board's report | Every float blank, integers fine | nano.specs printf drops floating point support
Clap trigger | LED on forever, script timed out | Threshold sized next to a wall, too high once it was gone
Weak transient warning | Loud clap called marginal | DC offset in the noise estimate, not real room noise
Notes: None of these announced themselves. Not one produced an error message. That is the honest engineering slide, and it is worth saying that this is what most of the debugging time went to.
The blank float one is a nice puzzle to pose to the audience: every integer printed correctly and every float printed nothing. That exact pattern is the fingerprint of the small printf implementation linked with nano.specs, which omits float support unless you ask for it. Fixed by formatting floats with integer arithmetic instead, so it cannot come back from a build setting.
What worked as defence: commit before and after every regeneration so a diff exposes it, treat every compiler warning as guilty, and build self-checks that flag a bad result without needing to know the right answer.

## Slide 15
What is not done
• The board's own bearing has NEVER printed
fix is written and committed, but not flashed yet
• Ground truth covers two angles, three trials
a real validation plot needs a full sweep
• 315 degrees is worse than 0 degrees and unexplained
the array should have no bad directions
• Nothing is wireless, and there is one node
multi-node needs inter-node time sync, a hard problem itself
• Claps only, one second at a time
no continuous operation, no speech, no battery
Notes: Do not rush this slide and do not apologise through it. Being precise about what is unproven is what makes the proven parts credible.
The first item is the important one. The integer stages of the embedded port match the reference exactly, onset and analysis window were identical on all three captures, so find_clap is validated. But the arithmetic downstream of it has never produced a visible number on hardware. So describe the port as partly validated, never as working.
If asked when it will be done: the fix is committed, it needs a flash and one capture, and the comparison script is already written and tested.

## Slide 16
Next steps
• 1. Flash the current firmware, confirm the report prints
• 2. Run the board versus reference comparison on a fresh capture
• 3. Sweep eight angles, five trials each, produce the validation plot
• 4. Then choose a direction:
multi-node cross-bearing | continuous operation | sources harder than claps
Notes: Steps 1 and 2 block everything else, and step 2 is already written and tested against synthetic data, so it is ready the moment the firmware is flashed.
Close by naming the decision you actually want input on: which of the three directions in step 4 is most useful to the group. Multi-node is the most interesting but it needs time synchronization between nodes, which is a substantial problem in its own right and worth being explicit about rather than assuming.
Then stop and take questions.

## Slide 17
Backup
for questions
Notes: Everything after this point is for questions, not for the main flow.

## Slide 18
Backup: why GCC-PHAT and not plain cross correlation
• Plain cross correlation is dominated by whatever frequencies are loudest
• A clap is broadband but very uneven, and a room colours it further
• PHAT divides out the magnitude and keeps only phase
• That gives a sharp correlation peak instead of a broad one
• Peak is then interpolated for sub-sample resolution
Cost: PHAT is noisier at low SNR, since it trusts quiet frequencies as much as loud ones
Notes: Only if asked. The honest trade is in the last line: PHAT whitens everything, so at poor SNR it is weighting noise-dominated bins as heavily as clean ones. For a loud clap in a quiet room that is a good trade, which is the case this project targets.

## Slide 19
Backup: the signal chain in detail
• PDM mic at 2.4 MHz, one bit per clock
• DFSDM sinc3 filter, oversampling ratio 150, gives 16 kHz
• Each 32-bit filter result is shifted right by 8 to make int16 PCM
• DMA in circular ping-pong halves, so capture never stops to copy
• All four channels drained as ONE aligned frame
That last point is what protects channel alignment, and GCC-PHAT depends on it entirely
Notes: The frame point is the subtle one. The code acts only when all four channels have flagged the same buffer half, then treats all four identically. If channels were handled independently, a clap arriving at the wrong moment could start one channel a frame ahead of another, and the estimator would read that bookkeeping error as acoustic delay.
It is also why the warm-up discard is one global counter rather than four per-channel counters.

## Slide 20
Backup: why the array is planar, and what that costs
• Four mics in a plane give BEARING only, not elevation
• A source above the plane is indistinguishable from its mirror below
• Elevation would need a non-planar layout, for example a tetrahedron
• For a node on a ceiling or a wall, bearing in the plane may be enough
This is the one limitation that is expensive to undo later
Notes: Worth raising with the group rather than defaulting into it. If the eventual deployment wants elevation, the array shape has to change, and every geometry number and the mounting change with it. Cheap to decide now, expensive to retrofit.

## Slide 21
Backup: how captures are stored
• captures / session / angle / trial
• A session is one sitting with one room setup
• Session notes record the port, the geometry and the wall distance
• The board's own report is saved beside the samples that produced it
That is what makes board versus reference comparison possible after the fact
Notes: The room setup is grouped by session because it is a property of the data, not of the run. The wall distance determined whether a whole session was trustworthy, so it lives with the captures.
Saving the board's report next to the samples was a late addition and it mattered: without it the report scrolled past in the terminal and was gone, because only one process can hold the serial port so you cannot watch it in a terminal at the same time.